## Slide 1
LEAN SIX SIGMA · DMAIC PROJECT
Improving Energy Efficiency and Reliability of Data Centers
An industry-level case built only on published, sourced data
Data cut-off: 30 September 2026 · Latest source: Uptime Global Data Center Survey 2026
Notes: Structure follows the two example documents: a full report (PDF) and a per-stage DMAIC deck. All numbers are from cited public sources; arithmetic is marked "computed".

## Slide 2
Project at a glance
Source: [1] Uptime Global Data Center Survey 2026
2
Real data only
Every number comes from a cited public source, with a clickable link.
No simulated or invented data; calculations are labelled "computed".
No pilot was run: the Improve stage uses published results and transparent projections.
PUE
1.52
baseline → target ≤ 1.40
Outage incidence
47%
baseline → target ≤ 35%
Avoidable outages
89%
baseline → target ≤ 75%
Water-use tracking
53%
baseline → target ≥ 79%
Four CTQs, baseline (2026) vs project target
Notes: Baselines are the Uptime Global Data Center Survey 2026. Targets are design choices anchored to cited benchmarks.

## Slide 3
Why data centers?
Source: [5] LBNL 2024 U.S. Data Center Energy Report · [12] Berkeley Lab news · [1] Uptime Global Data Center Survey 2026
3
176 TWh
U.S. data-center electricity in 2023, up from 58 TWh in 2014 (4.4% of U.S. electricity)
325–580 TWh
Projected U.S. data-center electricity in 2028 (6.7%–12.0% of U.S. electricity)
79%
of operators say management is at least somewhat concerned about cost
19%
of operators with a significant outage put its cost above $1 million (2026)
27%
of operators work in data centers older than 15 years, which slows efficiency gains
Notes: LBNL: 176 TWh in 2023 = 4.4% of US electricity; 325-580 TWh in 2028 (6.7%-12.0%). Uptime 2026: cost concern 79% (at least somewhat concerned); 19% of significant outages cost >$1M.

## Slide 4
D
Define: problem statement and CTQs
Source: [1] Uptime Global Data Center Survey 2026
4
Problem statement
Industry-average performance is below target on all four CTQs: PUE 1.52; 47% of operators had an impactful outage in three years; 89% of impactful outages were avoidable; only 53% track water use.
CTQ metrics
PUE = total facility energy ÷ IT energy. Outage incidence = % of operators with ≥ 1 impactful outage in 3 years. Preventability = % of outages avoidable. Water tracking = % of operators collecting water data.
Process constraint
Easy efficiency gains (containment, setpoints, controls) are already taken; legacy sites are costly to retrofit; staff and power availability are limited.
Notes: PUE definition: total facility energy divided by IT equipment energy (The Green Grid, 2007) as described by Uptime.

## Slide 5
D
Define: specifications and targets
Sources (full list on last slide): [1] · [8] · [9] · [5]
5
CTQ | Baseline 2026 | Individual spec | Project target | Basis
PUE | 1.52 | Site ≤ 1.5 | Average ≤ 1.40 | German limit for existing sites (1.5, 2027); LBNL modelled U.S. average 1.4
Outage incidence | 47% | No serious/severe outage | ≤ 35% per 3 years | Needs ~29% of avoidable outages eliminated (computed)
Outage preventability | 89% avoidable | Each outage reviewed | ≤ 75% avoidable | Rose 80% → 89% since 2024
Water-use tracking | 53% | Site reports annual use | ≥ 79% of sites | Parity with PUE tracking (79%)
Notes: Targets are author design choices anchored to cited benchmarks: 1.40 equals the LBNL modelled U.S. average (2023) and the proposed German 2030 limit; 79% equals the current PUE-tracking share.

## Slide 6
D
Define: scope and SIPOC
6
Suppliers
Utility · equipment vendors · water utility · IT tenants · staff and contractors
Inputs
Grid power · IT load · cooling water · procedures · maintenance
Process
Receive power → back up → power IT → remove heat → monitor → meter and report
Outputs
Available IT capacity · PUE / WUE · outage log
Customers
Business users · regulators · community and investors
In scope: power chain, cooling and heat rejection, procedures, metering and reporting. Out of scope: construction, IT applications, server purchasing, pricing.
Notes: Scope is the facility-management process. Roles are proposed design choices.

## Slide 7
M
Measure: data collection methodology
Source: [1] Uptime Global Data Center Survey 2026 · [6] Google PUE data · [5] LBNL 2024 U.S. Data Center Energy Report
7
Primary data
Uptime Institute Global Data Center Surveys 2025 and 2026 (>800 owners and operators each; PUE n=644 in 2026, outage n=715).
Benchmarks
Google measured fleet PUE (quarterly, 2019–2026); LBNL modelled U.S. PUE, WUE and energy.
Definitions
Kept exactly as published; no re-definition after seeing results.
Limitations
Self-reported; not a random sample; PUE differs by boundary; small samples for outage cost (n=77).
Notes: Limitations: self-reported survey, not a random sample (52% of respondents in North America and Europe), PUE for largest site, LBNL values are modelled.

## Slide 8
M
CTQ 1: industry PUE, 2007–2026
Source: [2] Uptime Global Data Center Survey 2025 · [1] Uptime Global Data Center Survey 2026
8
Chart: Weighted average annual PUE
| 2007 | 2011 | 2014 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026
Average PUE | 2.5 | 1.98 | 1.65 | 1.58 | 1.67 | 1.59 | 1.57 | 1.55 | 1.58 | 1.56 | 1.54 | 1.52
2.50 → 1.52
2007 to 2026: most of the drop came before 2014
−0.13
2014 to 2026 (1.65 → 1.52): only 12 years of slow progress
Notes: Series: 2.50 (2007), 1.98 (2011), 1.65 (2014), 1.58 (2018), 1.67 (2019), 1.59, 1.57, 1.55, 1.58, 1.56, 1.54, 1.52 (2026). Note the category axis is not evenly spaced in time before 2018. 1.65 to 1.52 = -0.13 over 12 years (computed).

## Slide 9
M
CTQ 1: where the 1.52 sits
Source: [1] Uptime Global Data Center Survey 2026 · [5] LBNL 2024 U.S. Data Center Energy Report · [6] Google PUE data · definitions differ
9
Chart: 
| Industry avg 2026 | Largest site avg 2026 | LBNL modelled U.S. 2023 | Project target | Google fleet 2025 | Google Singapore
PUE | 1.52 | 1.45 | 1.4 | 1.4 | 1.09 | 1.12
23%
of respondents already run a data center below PUE 1.3
0.52 vs 0.09
overhead per kWh of IT: industry vs Google fleet (83% less)
Notes: Uptime largest-site average 1.45; 23% of respondents below 1.3; LBNL modelled U.S. 1.4 (2023, assumes systems run as designed); Google fleet 1.09 (2025 TTM), Singapore 1.12 (Q2 2026 TTM).

## Slide 10
M
CTQ 2: impactful-outage incidence
Source: [1] Uptime Global Data Center Survey 2026
10
Chart: 
| 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026
Share with impactful outage | 74 | 69 | 60 | 55 | 53 | 50 | 47
47%
had ≥ 1 impactful outage in 3 years (95% CI 43%–51%, computed)
p = 0.25
2025 → 2026 change (50% → 47%) is not statistically significant: progress has slowed
Notes: Share of operators with an impactful outage in the past three years: 74, 69, 60, 55, 53, 50, 47 percent (n = 494, 730, 730, 781, 768, 754, 715). 95% CI for 2026: 43%-51% (computed).

## Slide 11
M
CTQ 2: severity and cost of outages
Source: [1] Uptime Global Data Center Survey 2026 · [2] Uptime Global Data Center Survey 2025
11
Chart: Severity, 2026 (n=715)
| 5 Severe | 4 Serious | 3 Significant | 2 Minimal | 1 Negligible
% of outages | 3 | 7 | 17 | 32 | 41
Chart: Cost of most damaging outage
| 2024 | 2025 | 2026
< $100k | 46 | 43 | 29
$100k–$1M | 33 | 37 | 52
> $1M | 20 | 20 | 19
Notes: Severity 2026 (n=715): 41/32/17/7/3 percent for categories 1-5. Cost of most damaging outage: 2024 (n=91) 46/33/20; 2025 (n=94) 43/37/20; 2026 (n=77) 29/52/19 percent. Percentages as printed; rounding.

## Slide 12
M
CTQ 3 and 4: preventability and water tracking
Source: [1] Uptime Global Data Center Survey 2026 · [2] Uptime Global Data Center Survey 2025
12
Chart: Outages judged avoidable
| 2024 | 2025 | 2026
Avoidable | 80 | 87 | 89
Chart: Operators collecting each metric
| Energy use | PUE | Water use
2025 | 84 | 74 | 47
2026 | 87 | 79 | 53
89% of impactful outages could have been avoided with better management, processes or configuration. Water is tracked by 53% vs 79% for PUE.
Notes: Avoidable outages: 80% (2024), 87% (2025), 89% (2026). Tracking 2025 vs 2026: energy 84 to 87, PUE 74 to 79, water 47 to 53 (n = 617 / 593). Water change z = 2.09, p = 0.037 (computed).

## Slide 13
M
Control chart: industry PUE (I-MR)
Source: [2] Uptime Global Data Center Survey 2025 · [1] Uptime Global Data Center Survey 2026 · limits computed
13
Chart: 
| 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026
PUE | 1.67 | 1.59 | 1.57 | 1.55 | 1.58 | 1.56 | 1.54 | 1.52
UCL 1.652 | 1.652 | 1.652 | 1.652 | 1.652 | 1.652 | 1.652 | 1.652 | 1.652
CL 1.573 | 1.573 | 1.573 | 1.573 | 1.573 | 1.573 | 1.573 | 1.573 | 1.573
LCL 1.493 | 1.493 | 1.493 | 1.493 | 1.493 | 1.493 | 1.493 | 1.493 | 1.493
Target 1.40 | 1.4 | 1.4 | 1.4 | 1.4 | 1.4 | 1.4 | 1.4 | 1.4
Control limit parameters
Centre line 1.573; UCL 1.652; LCL 1.493
Statistical interpretation
All 8 points are inside the limits: PUE is a stable process improving gradually, not a step change.
At −0.0093 per year, reaching 1.40 would take about 13 years (computed).
Notes: Individuals chart: CL = mean of 8 points; limits = CL +/- 2.66 x average moving range. All points within limits: stable process. Regression slope 2020-2026 = -0.0093/yr.

## Slide 14
M
Control chart: outage incidence (p-chart)
Source: [1] Uptime Global Data Center Survey 2026 · limits computed
14
Chart: 
| 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026
Share with outage % | 74 | 69 | 60 | 55 | 53 | 50 | 47
UCL | 64.1 | 62.9 | 62.9 | 62.8 | 62.8 | 62.9 | 63
p-bar 57.5% | 57.5 | 57.5 | 57.5 | 57.5 | 57.5 | 57.5 | 57.5
LCL | 50.8 | 52 | 52 | 52.2 | 52.1 | 52.1 | 51.9
Target 35% | 35 | 35 | 35 | 35 | 35 | 35 | 35
Statistical interpretation
2020–2022 lie above and 2025–2026 below the control limits: a real, sustained improvement.
2020 vs 2026: z = 9.35, p < 0.001.
2025 vs 2026: p = 0.25 — the recent change is within noise.
Reaching 35% needs a deliberate programme, not just the trend.
Notes: p-chart: p-bar = n-weighted mean 57.5%; limits = p-bar +/- 3 sqrt(p(1-p)/n) using each year n. 2020-2022 above UCL; 2025 and 2026 below LCL. z(2020 vs 2026) = 9.35.

## Slide 15
A
Analyze: fishbone diagram
Source: [1] Uptime Global Data Center Survey 2026 · [3] Uptime Outage Analysis 2025
15
Notes: Every entry is a published figure: hiring 53%, electrical skills gap 38%, retention issues 33%, procedures 85% of human-error outages, 89% avoidable, 27% of sites >15 years, water tracked 53%, server utilisation tracked ~42%, cost concern 79%, capacity forecasting 76%.

## Slide 16
A
Analyze: where outages come from
Source: [1] Uptime Global Data Center Survey 2026
16
56%
of impactful outages have power as the primary cause (2026, n=85)
Power has been the top cause every year since 2020. The 2025 dip (45%) looks like an outlier.
Chart: Drivers of power-related IT outages (n=129; not additive)
| UPS failure | Transfer-switch failure | Generator failure
% of power-related outages | 39 | 34 | 28
Notes: 2026: power 56% of primary causes (n=85; 45% in 2025, 54% in 2024). Power-related IT outages (n=129, multiple answers): UPS 39%, transfer switch 34%, generator 28%. Uptime cautions that the 2025 power share looked unusually low.

## Slide 17
A
Analyze: root-cause verification
Sources (full list on last slide): [2] · [1] · [6] · [3] · [7]
17
Suspected cause | Published comparison | Effect
Older facilities | Sites built in last ~5 years: PUE 1.48 vs 1.54 for all (2025) | −0.06
Small scale | ≥ 20 MW sites: 1.44 vs 1.54 (2025) | −0.10
Hot climate | Google Singapore 1.12–1.15 vs fleet 1.09 | +0.03 to +0.06
Seasonal load | Google fleet Q3 mean 1.120 vs Q4 1.084 (computed) | +0.036
Uncontrolled cooling | ML cooling control: −40% cooling energy, −15% PUE overhead | −15% overhead
Procedures | 85% of human-error outages involve ignored or flawed procedures | 85%
Power chain | UPS 39%, transfer switch 34%, generator 28% of power outages | 56% of causes
Notes: Newer sites 1.48 vs 1.54 (2025 survey); >=20 MW 1.44 vs 1.54 (2025); largest site 1.45 vs 1.52 (2026); Google Singapore Q2 2026 TTM 1.12 and 1.15 vs fleet 1.09; Q3 mean 1.120 vs Q4 1.084 (computed from 30 quarters).

## Slide 18
A
Analyze: why chains 1 and 2
Source: [1] Uptime Global Data Center Survey 2026 · [2] Uptime Global Data Center Survey 2025 · [3] Uptime Outage Analysis 2025 · synthesis of cited evidence
18
PUE stuck near 1.5
Fact: the industry average moved only 1.58 → 1.52 in 8 years.
1
Cheap gains (containment, setpoints, controls) were taken by 2014
2
Deeper upgrades in live legacy sites are costly and disruptive
3
27% of sites are > 15 years old and kept for capacity
4
Cooling is often controlled by fixed rules
5
No site-level efficiency roadmap
Root cause: easy gains exhausted; legacy sites stay without a retrofit plan.
Outages still frequent
Fact: 47% of operators had an impactful outage in 3 years.
1
Power is the top cause (56%)
2
UPS, transfer switches and generators fail most
3
Equipment not tested or operated as configured
4
85% of human-error outages involve procedures
5
Skills shortage: 53% cannot hire
Root cause: weak procedural discipline and testing on the power chain.
Notes: Why-chains are a synthesis of cited evidence, not measured facts.

## Slide 19
A
Analyze: why chains 3 and 4
Source: [1] Uptime Global Data Center Survey 2026 · [3] Uptime Outage Analysis 2025 · [5] LBNL 2024 U.S. Data Center Energy Report · synthesis of cited evidence
19
Preventability rising (80 → 89%)
Fact: 89% of impactful outages are judged avoidable.
1
Redundancy is widespread (44% 2N, 40% N+1)
2
Redundancy only works if configured and tested
3
Configuration and change control are inconsistent
4
Training and testing are under-funded
5
Hardware bought without process investment
Root cause: physical redundancy is not paired with operational discipline.
Water blind spot
Fact: 47% of operators do not track water use.
1
Water tracking is driven by regulation and public pressure
2
PUE is the headline KPI; water is outside it
3
PUE and WUE trade off (evaporative cooling saves energy)
4
Trade-offs are invisible without site-level data
5
Water is not a standard facility KPI
Root cause: water use is outside the standard KPI set.
Notes: Why-chains are a synthesis of cited evidence.

## Slide 20
I
Improve: countermeasures tied to verified causes
Sources (full list on last slide): [1] · [2] · [3] · [7] · [5]
20
Verified root cause | Countermeasure | Published evidence
Easy gains exhausted; legacy sites | Containment, higher supply temperature, better controls; retire worst sites | First-wave measures took PUE 2.50 → 1.65 (2007–14); new builds reach ≤ 1.3
Fixed-rule cooling | ML setpoint recommendations, advisory mode first | −40% cooling energy, −15% PUE overhead; only 31% of operators allow AI setpoints
Power-chain failures | Preventive maintenance and periodic transfer tests | UPS 39%, switch 34%, generator 28% of power outages
Procedures ignored or flawed | SOP/MOP/EOP library, checklists, change gates | 85% of human-error outages involve procedures
Skills shortage | Structured training; trade-school partnerships | 53% report hiring difficulty; electrical gap 38%
Water outside KPI set | Meter water; report WUE next to PUE | Modelled U.S. WUE ≈ 0.36 L/kWh; hyperscale 0.1–0.3
Notes: Evidence: PUE 2.50 to 1.65 (2007-2014) from first-wave measures; ML cooling -40% cooling energy, -15% PUE overhead; 71% trust AI for analytics vs 31% for setpoint control; power-chain failures 39/34/28; 85% procedures; LBNL WUE 0.36 L/kWh average, hyperscale 0.1-0.3.

## Slide 21
I
Improve: solution priority
21
Solution | Expected impact | Effort | Priority
Procedure discipline + change control | High | Low–Medium | Quick win
Power-chain test programme | High | Medium | Quick win
Water metering and WUE reporting | Medium | Low | Quick win
Cooling controls / ML advisory | Medium | Medium | Major project
Retrofit or retire legacy sites | High | High | Major project
Target improvement goal
PUE 1.52 → ≤ 1.40
Outages 47% → ≤ 35%
Avoidable 89% → ≤ 75%
Water tracking 53% → ≥ 79%
Ratings are the author's judgement, not data.
Notes: Impact and effort ratings are the author's qualitative judgement (marked as such), informed by the cited evidence; they are not measured data.

## Slide 22
I
Improve: how far can controls take PUE?
Source: [1] Uptime Global Data Center Survey 2026 · [7] DeepMind cooling blog · [6] Google PUE data · computed
22
Chart: 
| Baseline 2026 | Overhead −15% (DeepMind result) | Overhead −23% (needed for 1.40) | Google fleet 2025
PUE | 1.52 | 1.442 | 1.4 | 1.09
A projection, not a pilot result
A 15% overhead cut (as at the Google site) would give PUE 1.442.
Reaching 1.40 needs a 23% overhead cut.
Control optimisation alone is not enough: combine with retrofit or retirement of the least efficient sites.
Google Singapore (1.12–1.15) shows ≤ 1.15 is possible in the tropics at hyperscale.
Notes: PUE = 1 + overhead. 1 + 0.52 x 0.85 = 1.442. Needed overhead 0.40 => 23.1% reduction. Google overhead 0.09 is 83% below the industry 0.52.

## Slide 23
I
Improve: 12-week action plan (proposed)
23
1
Define
Weeks 1–2
Confirm charter, CTQs, owners
2
Measure
Weeks 3–4
12 months of PUE/WUE, outage log, procedure audit
3
Analyze
Weeks 5–7
Site I-MR charts; Pareto of own outage causes
4
Improve
Weeks 8–10
Containment, controls, test plan, standard work
5
Control
Weeks 11–12
Charts, owners, reaction plans, handover
The project team's job ends at handover; process owners carry the controls forward.
Notes: Proposed cadence for an operator adopting the method. Not executed at a real facility, so no measured after-results are claimed.

## Slide 24
C
Control: control plan
24
CTQ | Standard | Chart / frequency | Owner | Trigger and response
PUE | Site ≤ 1.5; portfolio avg ≤ 1.40 | I-MR, monthly (TTM reported) | Facility Engineering | Point outside limits or 8 above centre line: review controls, containment, meters in 5 days
Outage incidence | ≤ 35% per 36 months; zero serious/severe | p-chart, quarterly | Operations | Any impactful outage: root-cause review; serious/severe: executive review
Preventability | ≤ 75% avoidable; tests 100% on schedule | Monthly tests done vs planned | Procedures owner | Missed test or deviation: corrective action and retraining
Water tracking | ≥ 79% of sites report WUE | Quarterly coverage | Sustainability | Missing meter or data: fix plan within one quarter
Notes: Numeric limits for a site must come from that site's own first 12 months of data. Roles are proposed.

## Slide 25
C
Control: a real control chart on measured PUE
Source: [6] Google PUE data · limits computed
25
Chart: 
| 2019 |  |  |  | 2020 |  |  |  | 2021 |  |  |  | 2022 |  |  |  | 2023 |  |  |  | 2024 |  |  |  | 2025 |  |  |  | 2026 |
Fleet quarterly PUE | 1.09 | 1.11 | 1.13 | 1.09 | 1.09 | 1.11 | 1.13 | 1.09 | 1.09 | 1.1 | 1.12 | 1.09 | 1.09 | 1.1 | 1.12 | 1.08 | 1.08 | 1.1 | 1.12 | 1.08 | 1.08 | 1.1 | 1.11 | 1.08 | 1.08 | 1.1 | 1.11 | 1.08 | 1.08 | 1.1
UCL 1.144 | 1.144 | 1.144 | 1.144 | 1.144 | 1.144 | 1.144 | 1.144 | 1.144 | 1.144 | 1.144 | 1.144 | 1.144 | 1.144 | 1.144 | 1.144 | 1.144 | 1.144 | 1.144 | 1.144 | 1.144 | 1.144 | 1.144 | 1.144 | 1.144 | 1.144 | 1.144 | 1.144 | 1.144 | 1.144 | 1.144
CL 1.098 | 1.098 | 1.098 | 1.098 | 1.098 | 1.098 | 1.098 | 1.098 | 1.098 | 1.098 | 1.098 | 1.098 | 1.098 | 1.098 | 1.098 | 1.098 | 1.098 | 1.098 | 1.098 | 1.098 | 1.098 | 1.098 | 1.098 | 1.098 | 1.098 | 1.098 | 1.098 | 1.098 | 1.098 | 1.098 | 1.098
LCL 1.051 | 1.051 | 1.051 | 1.051 | 1.051 | 1.051 | 1.051 | 1.051 | 1.051 | 1.051 | 1.051 | 1.051 | 1.051 | 1.051 | 1.051 | 1.051 | 1.051 | 1.051 | 1.051 | 1.051 | 1.051 | 1.051 | 1.051 | 1.051 | 1.051 | 1.051 | 1.051 | 1.051 | 1.051 | 1.051 | 1.051
What it teaches
All 30 quarters sit inside the limits: a stable, well-controlled process.
Summer (Q3) is always highest: 1.120 vs 1.084 in Q4 (computed).
So chart trailing-twelve-month PUE, or allow for seasonality, to avoid false alarms.
Notes: Google fleet quarterly PUE, 2019Q1-2026Q2 (30 points). CL 1.098, UCL 1.144, LCL 1.051 (individuals chart). Q3 mean 1.120, Q4 mean 1.084.

## Slide 26
C
Control: transfer to process owners
26
The project team's job ends at handover. From there, four owners carry it forward.
Facility Engineering Manager
Owns PUE standards and cooling controls; reviews the monthly I-MR chart.
Operations Manager
Owns the outage log, p-chart and power-chain test schedule.
Procedures Owner
Owns SOP/MOP/EOP library, training and change control.
Sustainability Manager
Owns water metering, WUE reporting and the KPI dashboard.
Notes: Roles are proposed design choices.

## Slide 27
Operational impact per 1 MW of IT load
Source: [1] Uptime Global Data Center Survey 2026 · computed
27
13,315 MWh
facility energy per year at PUE 1.52
12,264 MWh
facility energy per year at PUE 1.40
1,051 MWh
saved per year (−7.9%)
Outages: 71% of significant outages cost ≥ $100,000 and 19% exceed $1 million. Going from 47% to 35% incidence means about 12 fewer operators in 100 affected per three years.
To convert to money, use the site's verified tariff, water price and outage-cost records.
Notes: 1 MW x 8,760 h = 8,760 MWh IT. Facility energy = IT x PUE. No money value is claimed: it requires a verified local tariff.

## Slide 28
Conclusion
PUE is a stable process improving by less than 0.01 a year; 1.40 needs retrofit, not just control tuning.
Outage incidence fell 74% → 47%, but the latest change is not significant and 89% of outages are still avoidable.
Power-chain equipment and procedural discipline dominate the causes.
All figures are published aggregates: re-run Measure and Analyze on your own site data before fixing targets.
Sources are listed on the next slide.
Notes: Main limitation: published aggregates, no pilot.

## Slide 29
Sources (click to open)
29
[1] Uptime Institute (Jul 2026). Global Data Center Survey 2026.
Open source
[2] Uptime Institute (Jul 2025). Global Data Center Survey 2025.
Open source
[3] Uptime Institute (May 2025). Annual Outage Analysis 2025 (press release).
Open source
[4] Uptime Institute (May 2026). Annual Outage Analysis 2026 (press release).
Open source
[5] Shehabi et al. (Dec 2024). 2024 United States Data Center Energy Usage Report, LBNL.
Open source
[6] Google Data Centers. Power usage effectiveness (to Q2 2026).
Open source
[7] Evans & Gao (2016). DeepMind AI Reduces Google Data Centre Cooling Bill by 40%.
Open source
[8] White & Case (2023). German Energy Efficiency Act: data center requirements.
Open source
[9] Gleiss Lutz (Feb 2026). EnEfG draft amendment.
Open source
[10] Uptime Institute (Jul 2026). 16th Annual Survey press release.
Open source
[11] Uptime Intelligence (Jun 2026). Annual outage analysis 2026.
Open source
[12] Berkeley Lab News (Jan 2025). Report on U.S. data center electricity demand.
Open source
Notes: All accessed 28-30 September 2026.